TP2x ® 20.2
User’s Manual

   Finite Element Method
Full Description of all Entities,
Input and Output Data, Error Messages
and Tips.

User Tip:

You can page and search >

1.	via page numbers at contents
2.	via red marked chapter numbers
3	via chapter numbers at subject index
4.	via 'Go To' command at Acrobat Reader
-	figures via figure numbers

Read first examples for
Linear Static's	>	helpstat.pdf
Non-Linear Static's >	helpnoli.pdf
Linear Dynamic's >	helpdyna.pdf
Potential	>	helppoti.pdf

Copyrights © IGF 1997-1998, 1999, 2002-2004, 2007, 2008, 2015, 2017, 2019,2021
Ingenieursozietät Prof. Dipl.-Ing. P. Groth, Prof. Dipl.-Ing. H. Faiss,
Ingenieurleistungen, Drosselweg 57/2, D-72793 Pfullingen

Co-Autoren:	Dipl.-Ing. Karsten Löhr, MGT TU Chemnitz (Abschn. 8.3.9);
2003	Dipl.-Ing. Andreas Mayr; TEP TU München (Kap. 11)

OPTION-FILE TP2000 (Attention!! only values can be changed) (DATABASE definition see at the bottom!) ----------------------------------------------------- Nr.< values >( options ) meaning ----------------------------------------------------- General: ----------------------------------------------------- 1 ......2000 ( > 800 ) utilizable memory in MB REL 10.i 2 ........MM (CM,DM,M,UM) length unit, UM = micrometer 3 ........ N (P,KP,MP ) force unit . (N,UN ) UN = micro Newton 4 ........ ( C,F,K ) temperature unit 5 .........0 ( 1 ) 1: normal vector plane elements, orientation . at 1st element 6 .........0 ( 1 ) 1: read table data TAB via fre file 7 .......0.1 ( > 0.0 ) merge distance eFEA/FEMAP/MEDINA contact conditions . (node pairs, master/slave) or element plane check 8 .......0.0 ( x ) x=G1, 1.gap(+x)/shrinking value(-x) . eFEA/FEMAP/MEDINA contact conditions 9 .......0.0 ( x ) x=G2, 2.gap(+x)/shrinking value(-x) . eFEA/FEMAP/MEDINA contact conditions 15 .......0.0 ( x ) x=gap diameter diff. eFEA/FEMAP/MEDINA cyl. contact 16 .........0 ( i ) contact point node number (inside) for Opt.(15) 10 .......0.0 ( x ) x=F1,1.gliding friction angle [rad] at . eFEA/FEMAP/MEDINA contact conditions 11 .......0.0 ( x ) x=F2,2.gliding friction angle [rad] at FEMAP/MEDINA . eFEA/FEMAP/MEDINA contact conditions 13 .......0.0 ( x ) x=F3,1.static friction angle [rad] for FEMAP/MEDINA . eFEA/FEMAP/MEDINA contact conditions 14 .......0.0 ( x ) x=F4,2.static friction angle [rad] for FEMAP/MEDINA . eFEA/FEMAP/MEDINA contact conditions 19 .......0.0 ( x ) factor > 0.00001, eFEA/FEMAP/MEDINA . geometry gap is valid 12 .........0 ( 1,2 ) 1: add mid-side nodes, if not exist . 2: same as 1, however with constraints 17 .........0 ( i ) i: start node for bandwidth optimization 18 .........0 ( 1,2 ) 1: extension at MST for BEM or fluidic damping 20 .........1 ( i ) load-case number screw pre-stressing via beam gap 21 .......0.1 ( x ) sector angle (rad) at rot.sym. elements 1.0=0.1 22 .........0 ( i ) i:0,3,4,>4 element nbr. NEL per net with i digits . i=0 and >4 means 4, element number: Net*10^i + NEL 23 .........0 ( i ) i>0: start postprocessor after FEM-calculation . i = load-case number for the result representation 24 .........1 ( 1/0 ) at Opt.(23): deformed model of total displacements 25 ........21 ( i ) at Opt.(23):1 > total displacements contour . 21> averaged principle stresses as contour . 22> max. principle stresses as contour . 32> max. model error 26 .........4 ( i ) at Opt.(23):i = deformation factor in model percent 27 .........0 ( i ) at contact calculation: all load-cases 1-i are activ 28 .......0.0 ( x ) max. contact force at static friction>prog. canceled 29 .........0 ( 1 ) autom. temp. contact controll, if open in statics . repeat potential-statics loop ----------------------------------------------------- Measurement data: ----------------------------------------------------- 30 .........2 ( 1,2 ) 0:2D-geometry based on mask (name_g.mat) . 1:3D-shell model based on CAD or STL file . 2:3D-tetmesh model based on CAD or STL file 31 .........0 ( 1 ) 1:for 2D; define only 1 polygon as boundary surface . with holes 32 .........1 ( 0,1-4 ) 0:in plane data as deformation . 1:out of plane data as enforced displacement . 2:as 1, with defined constraints . 3:out of plane data as enforced displacement + rot. . 4:as 3, with defined constraints 33 .........1 ( >1 ) number of measurement steps without unloading 34 .........0 ( 1 ) 1:unloading in 1 step 35 ........0. ( > 0.0 ) desired element edge length (tet- or shell-mesh) 36 ........1. ( > 0.0 ) XDELTA = scale factor (X(unit) = pixel*XDELTA) 37 ........1. ( > 0.0 ) YDELTA = scale factor (Y(unit) = pixel*YDELTA) . if YDELTA=0 and XDELTA>0, YDELTA=XDELTA 38 .......1.0 ( > 0.0 ) priority element thickness at property ID 1 39 ..210000.0 ( > 0.0 ) priority Young’s modulus E at material ID 1 40 .......0.3 ( > 0.0 ) priority Poisson's ratio nu at material ID 1 41 .....0.001 ( > 0.0 ) factor to scale the measurement data 42 .........0 ( 1,2 ) 1:nonlinear material "von Mises" . 2:nonlinear material "Drucker-Prager" . DELTA-X for xz mask, if Opt.(42) = 0 43 .......0.0 ( > 0.0 ) 1.yield stress (v.Mises) at material ID 1, or . 1. cohesion C1 (Drucker-Prager) at material ID 1 or . DELTA-X for xy mask, if Opt.(42) = 0 44 .......0.0 ( > 0.0 ) stress ratio (v.Mises, Drucker-Prager) . at cinematic hardening . DELTA-Z for xz mask, if Opt.(42) = 0 45 .......0.0 ( > 0.0 ) 1.dilatancy angle (in degree) Drucker-Prager or . -1.0: xy reflection of mask and data 46 ......-1.0 ( > 0.0 ) 2.yield stress (v.Mises) or . 2:cohesion Drucker-Prager or . -1.0: xz reflection of mask and data 47 .......0.0 ( > 0.0 ) 2.dilatancy angle (degree) Drucker-Prager or . -1.0: yz reflection of mask and data 48 .........5 ( >2 ) number of iteration steps for nonlinear material 49 .........8 ( >5 ) used FEMAP release ----------------------------------------------------- Statics (linear and nonlinear) general ----------------------------------------------------- 50 ........ 0 ( 1,2,3 ) for 3 node edge loads in, 0: xy- (rot.symm.) . 1: yz-, 2: xz-, 3: xy-plane 51 .........0 ( 1 ) 1:calculated temperature field as load-case 1 52 .........6 ( 1 - 7 ) output file defination: . 7: binary, (for stresses see Opt.(95)) 53 .......0.0 ( > 0.0 ) rotational speed in rot/sec for centrifugal . forces at x-axis 54 .......000 ( 1-122 ) load-case number for Opt. 53 55 ........+0 ( +/- 1,2,3) model dead load in x,y,z, as load-case 1 56 ....... 00 ( 1-61 ) number of Fourier orders for Fourier elements 57 .......0.0 ( 0. - 360.) meridian plane angle PHI for result output of . Fourier elements 58 .......0.0 ( 1. - 360.) end angle at Opt.(57) (from - to) 59 .......0.0 ( 1. - 360.) increment angle at Opt.(57/58) 60 ........00 ( 1-61 ) valid number of orders in result output . Fourier elements 61 .......0.0 ( > 0.0 ) scale factor result output Fourier elements 62 .........2 (1,2,3 ) type of processing constraint equations CT32 . 1: FREE (additional input) 2: AUTO 3: RAND 63 ........10 (10 - max. ) max. number of contact iterations . set negative if all parts are completely supported 64 .......0.0 ( > 0.0 ) tolerance for singularity check step STEMA. 65 .....0.001 ( > 0.0 ) tolerance for singularity check equation solver 66 ........ 0 (1,>1=IALTM) processing type > variable constraint equations CT32 . 0: standard 1: old method 67 ........ 0 ( 1 ) element type 124 only (triangle / shell) . 1:D1=membrane thickness, D2=bending thickness 68 .........2 ( 2 - max. ) number of special beam loads per beam (STALA) 69 .........0 ( 1 ) 1: at special beam loads, line loads as CT45 (STALA) ----------------------------------------------------- Statics (list- and write options) ----------------------------------------------------- 70 .........$ ( i ) i: form feed character (new page) for line printer 71 ........45 ( 32/45 ) lines per page in diagnostics report file (8/12") 72 ........56 ( 36/56 ...) lines per page in output list file (8/12" or more) 73 .........2 ( 0,1,2,3,4) 0:no full diagnostics report, degrees of freedom list . 1:diagnostic report list . 2:same as 0, however without degrees of freedom list . 3:same as 0, however with degrees of freedom list . 1-1000 nodes . 4:same as 0, however with degrees of freedom list . each 10th node 74 .........0 ( 1 ) result general, 1: node values not sorted 75 .........2 ( 1,2 ) result list 1: without displacements . 2: as 1, without stresses 76 .........0 ( 1 ) result list 1: without reaction forces 77 .........0 ( 1 ) result list 1: without beam section forces and . deformations . 3: normal beam forces only 78 .........0 ( 1 ) result list 1: for nodes on free edges only 79 .........0 ( 1 ) result list 1: beam energy separated for FU,MU,MV,MW 80 .........0 ( 1 ) list output 1: list all used nodes . 2: list all used elements 3: both 81 .......400 ( 0 ) 2.list window: max. number of rows <= 455 . 0: no report (prt file) printed 82 .........0 ( 1 ) list output, 1: load sum per load-case 83 .........0 ( 1 ) list output, 1: print-plot Fourier synthesis 84 .......000 ( i= 1-122 ) all output suppressed for load-case i (from) 85 .......000 ( j= 2-122 ) all output suppressed for load-case j (to) 86 .........0 ( 1,2 ) 1: write input file name.fre as name.fmt for . ELIAS3.0, isotropic material only . 2: as 1, without restrictions, with STOP or CONTINUE 87 .........0 ( 1,2 ) 1:convert input file name.fre to ELIAS4-fre format . as name-4.fre, 2:as 1, with STOP or CONTINUE message 88 .........0 ( 1,2 ) 1: additional> write output to FEMAP neutral file . (formatted) . 2: as 1, without TPS10 format (name.erg) . -1/-2: as positive, however for MEDINA BOF . 3: as 1, write additional eFEA pch result file . (formatted) . -3: as 3, additional velocity + acceleration . 4: as 3, however at Solid Elemental Stress: . sig1/2/3 and phi1/2/3 89 .........1 ( 0,1,2 ) to Opt.(88) . 0: no nodal average stresses, model error only . 1: nodal average stresses Sigma_V und Sigma_Max only, . at MEDINA additional for mid-side nodes . 2: nodal average stresses for all types of stresses . 3: as 1, additional on mid-side nodes . 4: as 2, additional on mid-side nodes . (Very large ouput, for MEDINA only! Unnecessary, . values are interpolated in FEMAP) ----------------------------------------------------- Statics (stress and strain energy output) ----------------------------------------------------- 90 .........0 (1,2 ) 1: stress output on integration points . at axisysm. elements or at corner nodes at solids . 2: improved stress calculation for axissymm. elemts. 91 ........+3 (1-7, +/-3 ) ideal stress or strain hypothesis . 1: normal stress hypothesis . 2: shear stress hypothesis . 3: strain energy hypothesis (von Mises) . -3: switch to normal str. hyp. if pressure (neg. value) . 4: composite reserve factor or plastic strain . >3: strain output at nonlinear statics . 4: strain output at non-lin. statics as total strains . 5: at strain: plastic strains only . 6: at strain: elastic strains only . 7: at strain: all 3 strain types in one list 92 .........0 ( 1,2 ) section values at plane elements . 1: additional in result list . 2: no stresses, section values only 93 .........0 ( 1 ) section values elemental(0) or nodal(1) 94 .........1 (0,+-1,2,3 ) averaged node stresses in list file . 0: no incl. model error 1:top side only, 2:both sides . 3: same as 2, local in u,v,w without transformation . -: same as +, however max. nodal values in output 95 .........1 ( 1 - 5 ) write stress result file, nodal or elemental . 1: nodal average stresses as defined in Opt.(92-94) . 2: same as 1, add. elemental stresses in loc. coords . 3: same as 1, add. elemental stresses in glob.coords . 4: same as 1, additional specific strain energy . + main stresses 96 .......0.0 ( > 0.-90. ) type of average, active only, if Opt.(107-117) . is not used! . 0. : if all elements at node are in the same plane . >0.: max. angle tolerance to mean plane 97 .......0.0 ( > 0.-90. ) to Opt.(96) . >0.: max. angle tolerance based on 1st element plane 98 ..999999.0 ( > x=0. ) only stresses > x are printed, to reduce result list 99 .........0 ( 1 ) 1: no stress calculation for beam elements 100 .........0 ( 1 ) 1: no stress calculation for flat elements 101 .........0 ( 1 ) 1: no stress calculation for solid elements 102 .........1 ( 1 ) 1: axissymm. (1,7) stresses based on x,y,z 103 ........00 ( i= 1 - 99) stress calculation only for net i (from) 104 ........00 ( j= 1 - 99) stress calculation only for net j (to), max. 105 ........00 ( i= 1 - 99) calculate composite stresses for layer i (from) 106 ........00 ( j= 1 - 99) calculate composite stresses for layer j (to) 107 ........0. ( > 0. ) stress transformation, Euler angle THETA 108 ........0. ( > 0. ) stress transformation, Euler angle PSI 109 ........0. ( > 0. ) stress transformation, Euler angle PHI 110 ........00 ( 12,13,23 ) stress transformation, on plane xy,xz,yz 111 ........00 ( i= 1 - 99) net selection for Opt.(107-110), from i 112 ........00 ( j= 1 - 99) net selection for Opt.(107-110), to j 113 ........0. ( x > 0. ) X=factor, program cancel if Sig_ideal > Sig_pl*X . at non-linear v. Mises material or . ( p > 0. ) p=pressure in tubes, added to ideal stresses (beams) 114 ........0. ( D > 0. ) D=tube diameter for Opt.(113) 115 ........0. ( s > 0. ) s=tube thickness for Opt.(113) 116 ........00 ( i= 1 - 99) net selection for Opt.(113-115), form i 117 ........00 ( j= 1 - 99) net selection for Opt.(113-115), to j 118 .........0 ( 1 ) stress print-plot in result list 119 .........0 ( 1,2,3 ) reflection plane (1=xz; 2= yz; 3=xy) for stress . calculation in reflected part 120 .........1 ( 1 ) strain energy per net in % in result list, . as specific strain energy via Opt.(95) = 4 ----------------------------------------------------- Statics (load-case superposition) ----------------------------------------------------- 121 ......1001 ( LLJJJIKKK) I =< 9= set ID constraint equations . KKK =<497=set ID load-case, or from KKK to JJ by LL . JJJ =<497=load-case ID to; LL = increment 122 .......1.0 ( x ) factor x to Opt. 121 123 ......1002 ( LLJJJIKKK) load-case number (if not exist, no superposition!) 124 .......1.0 ( x ) factor x to Opt. 123 125 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 126 .......1.0 ( x ) factor x to Opt. 125 127 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 128 .......1.0 ( x ) factor x to Opt. 127 129 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 130 .......1.0 ( x ) factor x to Opt. 129 161 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 162 .......1.0 ( x ) factor x to Opt. 161 163 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 164 .......1.0 ( x ) factor x to Opt. 163 165 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 166 .......1.0 ( x ) factor x to Opt. 165 167 .........0 ( LLJJJIKKK) next load-case as Opt.(121) 168 .......1.0 ( x ) factor x to Opt. 167 ----------------------------------------------------- Statics (output file superposition >LAFAK) ----------------------------------------------------- 131 .........0 ( 1 ) 1:RESTART new output file with result files superpos. 132 ..-------- ( 8 chars. ) name of 1sr output file without extension 133 ..-------- ( 8 chars. ) name of 2nd output file without extension 134 ........1. ( x ) factor x to Opt.(132) 135 ........1. ( x ) factor x to Opt.(133) 136 .........0 ( i= 1-122 ) 0=1, i: set ID load-case to Opt.(132) (from) 137 .........0 ( i= 1-122 ) 0=1, i: set ID load-case to Opt.(133) (from) 138 .........0 ( i= 2-122 ) to Opt.(132), until load-case i (to) 139 .........0 ( i= 2-122 ) to Opt.(133), until load-case i (to) 140 .........0 ( 1,2 ) for reflected part, type of symmetry . 1: SYM, 2: ANT, to Opt.(132) 141 .........0 ( 1,2 ) for reflected part, type of symmetry . 1: SYM, 2: ANT, to Opt.(133) 142 ........12 ( 12,13,23 ) reflection plane to Opt.(132), xy,xz,yz 143 ........12 ( 12,13,23 ) reflection plane to Opt.(133), xy,xz,yz ----------------------------------------------------- HPC Version solver: KEDA/OPTIM and LIGL/ELIMN parallelization MPI ----------------------------------------------------- 150 .........0 ( 1,0 ) 0=single proc., 1=IntelMPI parallel HPC . Linux only, openMP parallel not used, old ----------------------------------------------------- Statics (sort nodal and elemental data via load-cases >TSORT; extrem value calculation) ----------------------------------------------------- 151 .. ( 8 chars. ) name of binary output file without extension . if blank > actual project is valid 152 .........0 ( 1,2 ) 1: sort data, condition for EXTREM . 2: as 1, however with RESTART 153 ........+1 ( +/- 1,2 ) values to sort (beam and/or plane elements) 154 .......000 ( i= 1-122 ) output of max./min values load-case i 156 .........0 ( 1 ) 1: with result list of beam section values, stresses 157 .........0 ( 1 ) 1: with result list of reaction forces additional 158 ........00 ( i= 1-99 ) result list for net i only 159 .......050 ( max. 122 ) sort array for i load-cases, default 100 (i=0) 160 .........0 ( 1 ) 1: extreme value calculation, additional input required ----------------------------------------------------- Statics (nonlinear) ----------------------------------------------------- 170 .........1 ( 1 - 122 ) max. number of load steps, valid if > INPUT 171 .........0 ( 1,2,4 ) iterat.method, 0:Full Newton-Raphson FNR, 1:modif.MNR . 2:Full Radial Return FRR, OPT(186) NOLNEU = 1 . 4:Full Lagrange Rad.Return FLRD, large strains Shel34 172 .........0 ( 1 ) load steps, 0: as standard . 1: RAND(edge/surface)-load, calculate new increment . 2: at compression load FLRD, calculate new increment 173 .........0 ( 1,2 ) 0: without 1,2: with geometric stiffness matrix 174 .......000 ( > 0 ) max. number of iterations per load-step 175 ........5. ( i % ) convergence tolerance of Euclid’s norm to stop . iterations 176 ........00 ( > 0 ) max. number sub-iterations, FNR, LLRD + bar elements 177 .........0 ( 1,2,3 ) nonlinear material for beam elem. as principle . stresses, TP2000-hypothesis 1-3 178 .........0 ( 1 ) for beam elements only, type of material function . as step function = 0 . as linear function = 1 179 .........0 ( 1 ) beam elements only, 1:spring rate with curve fitting 180 .........0 ( 1 ) 1: yielding with cinematic hardening (80%) or type . factor in % e.g. 90 181 .........0 ( > 1 ) max. number of iteration steps yield material 182 .........0 ( 1 ) 1: without coordinate update (small deformations) 183 .........1 ( 1,2 ) 1: write output file for each load step (standard) . 2: write output file for each subiteration 184 .........2 ( 1,2 ) 1: write output file after last loadstep . 2: as 1, however without displacements of loadsteps 185 .........0 (1-3 ) RESTART with new input parameters . 1/2: save for RESTART . 3: as 2 with RAND(edge)-loading of deformed model . at RESTART 186 .........0 ( 1 ) NOLNEU= 1 new non-linear Radial Return Method FRR/D 187 .........1 ( 0,1 ) NPLAST= 0 elastic, 1 elastoplasic 188 .........0 (1-Opt(170)) i:change enforced displacement direction of loadstep i . (unloading), if negative full released at RC=1 189 .........0 (1-Opt(170)) i:change enforced displacement direction of loadstep i . (unloading), if negative full released at RC=1 190 .........0 (1-Opt(170)) i:change enforced displacement direction of loadstep i . (unloading), if negative full released at RC=1 191 .........0 ( 0, 1 ) 0 stress interpol. 1 calculated stress and strain ----------------------------------------------------- Potential problems ----------------------------------------------------- 192 ........01 ( -1,1,2 ) output file 1: formatted 2: binary . -1: temperature field as CT48-format to name.stz 193 .........1 ( 1 ) 1: with heat flux in output list and output file 194 .........1 ( 1 ) 1: output list as table, 0: no list 195 .........1 ( 1,2 ) to Opt.(194) non steady state field (transient) . 1: actual, 2: additional delta(p)-field 196 .........0 ( 1 ) 1: output list with print-plot 197 ........0. ( ABS (x) ) to Opt.(196), print values > x only 198 ........0. (z.B. t=20 ) t=ambient temperature at static run (temp.field - t) 199 ........00 ( > 0 ) max. number of iterations with non-linear material . for steady state temperature field calculation 200 .........0 ( 1,2 ) 1: with time step control, increase time step . until Opt.(202) is reached . 2: as 1, switch to automatic time step control . if Opt.(202) is reached; Opt.(201-205) are valid 201 .......0.2 ( <= 0.2 ) factor for time step control 202 .......0.5 ( > 0.0 ) min. limit value for time step control 203 .......1.0 ( > OPT 202) max. limit value for time step control 204 .......2.0 ( > 0.0 ) min. absolute value of temperature alteration 205 ......10.0 ( > OPT 204) max. absolute value of temperature alteration 206 .........0 ( > 0 ) RESTART none st. state potential with Opt.(207-209) 207 .......0.0 ( > 0. ) time step delta t 208 ........00 ( > 0 ) max. number of corrector iterations 209 ........0. ( > 0. ) end time Tmax 210 ........00 ( > 0 ) max. number of time steps ----------------------------------------------------- Dynamics (simultaneous method with full stiffness matrix >SIMIT) . fluidic damping in squeeze-film (air gap) ) ----------------------------------------------------- 212 .......0.0 ( > 0. ) air gap (squeeze film) distance [Um] 213 .......0.0 ( > 0. ) normal pressure in squeeze film [bar] 214 .......0.0 ( > 0. ) air pressure [bar] 215 .......0.0 ( > 0. ) mean value of free air displacement length [Um] 216 .......0.0 ( > 0. ) air viscosity at normal pressure [Um**2/sec] 217 .........0 ( > 0 ) number of start eigenvalue 218 .......0.0 ( > 0. ) selected active frequency [Hz] 219 .........0 ( > 0 ) max. number of calculated periods ----------------------------------------------------- Dynamics (simultaneous method with full stiffness matrix >SIMIT) . harmonic force or ground excitation (earthquake); . for RESTART with new data, additional input is required) ----------------------------------------------------- 220 .......010 ( max. 122 ) max. number of eigenvalues 221 ........15 ( max. 30 ) max. number of iterations, > 30 no sense 222 ......0.02 ( > 0. ) angle tolerance in [rad] as convergence tolerance 223 .......0.1 ( > 0. ) factor of eigenvalue normalization 224 .........1 ( 1,2,3 ) 1: amplitudes 2: energy 3: mass normalization 225 .........0 ( 1 ) 1: at free/free modue no characteristic vector output . for rigid body frequency = 0 226 .........1 ( 0 ) 0:without 1:with additional masses via load-case VN=99 227 ....123000 ( 123456 ) used degrees of freedom (vx ... dz is valid only) 228 .......-06 ( i < 0 ) exponent (10**x) tolerance check of orthogonality 229 .......50. ( x => 0. ) x= estimated 1st eigenfrequency (HZ) for free/free . x=0: without free/free 230 .....0.009 ( x > 0. ) tolerance EPS as degree of precision for free/free 231 .........0 ( 1 ) continue with modal excitation (MOTRA,MOERG, . additional input required ! 232 .........0 ( 1-NDMAX ) damper node or 1st node for double sided damper 233 .........0 ( 1-NDMAX ) 2nd node for double sided damper 234 .........0 ( 1 - 99 ) damper ID as Opt.(238) 235 .........0 ( 0,1,2 ) damping force 0:prop. displacement 1:prop. velocity . 2: prop. acceleration 236 ......0.00 ( x > 0. ) damping rate to Opt.(232 / 233) 237 .......001 ( I J K ) vector of single damper, IJK = XYZ . e.g. 111 = 1./1./1. - direction 238 .........0 ( 1 - 99 ) excitation ID, meaning: complete input . via OPT(239-257) . 0:excitation input via additional input name.zus 239 ........10 ( 0,1,2,10 ) type of excitation, 0-2: base-, . 10: force excitatation 240 .........0 ( 1-NDMAX ) >0: excitation node at force excitation (from) . 0: excitation proportional loading (to Opt.(241)) 241 .........0 ( 1 - 122 ) >0: load-case ID at excitation proprotional loading . 0: node difference at node string Opt.(240)(incr.) 242 .........0 ( 1-NDMAX ) end excitation node at node string Opt.(240-241)(to) 243 .......001 ( I J K ) excitation vector, IJK = XYZ . e.g. 111 = 1./1./1. - direction 244 .........1 ( 1,2,3 ) base excitation as 1:path, 2:velocity 3:ecceleration 245 ........00 ( 0,1 - 99 ) 0: without damper, i: damper ID to Opt.(234) 246 .......0.0 ( x > 0.0 ) force excitation amplitude 247 .......0.0 ( x 0.-360.) force excitation phase angle 248 .......0.0 ( x > 0.0 ) frequency characteristic: step amplitude difference 249 .........0 ( 1 ) 0: linear 1: logarithm. interpolation response . spectrum (Opt. 250-260) at base excitation 250 .......0.0 ( x > 0.0 ) const. excitation frequency at force excitation or . frequency curve (from) . or 1st response spectrum frequency at base excitation 251 .......0.0 ( x > 0.0 ) excitation frequency at force excitation (to) . or 2nd response spectrum frequency at base excitation 252 .......0.0 ( x > 0.0 ) excitation frequency at force excitation (increment) . or 3rd response spectrum frequency at base excitation 253 .......0.0 ( x > 0.0 ) degree of damping at force excitation . or 4th response spectrum frequency at base excitation . note: if more than 4 values > additional input req. 254 .......0.0 ( x > 0.0 ) 1st response value at 1st frequency (Opt. 250) 255 .......0.0 ( x > 0.0 ) 2nd response value at 2nd frequency (Opt. 251) 256 .......0.0 ( x > 0.0 ) 3rd response value at 3rd frequency (Opt. 252) 257 .......0.0 ( x > 0.0 ) 4th response value at 4th frequency (Opt. 253) ----------------------------------------------------- Dynamics (back transformation at dyn. excitation (SIMIT) in SUPHA or SUPEV) . (for 1 variant only; for more > additional input req.) ----------------------------------------------------- 261 .........0 ( 1/2 ) superposition at force excitation SUPHA 262 .........0 ( 1/2 ) superposition at base excitation SUPEV 263 ..-------- (8 chars. ) new header line at output list (max. 32 Zeichen) 264 ..-------- (8 chars. ) new header line at output list 265 ..-------- (8 chars. ) new header line at output list 266 ..-------- (8 chars. ) new header line at output list 267 ........0. (0. - 360. ) phase loop start angle (SUPHA) (from) 268 ........0. (1. - 360. ) phase loop end angle Opt.(267) (to) 269 ........0. (1. - 360. ) angle increment as step at Opt.(267-268) 270 ........0. (1. - 360. ) zero phase angle at force excitation 271 ........00 ( 1 - 99 ) variant ID at excitation (from) 272 ........00 ( 1 - 99 ) variant ID at excitation to Opt.(271) (to) 273 ........10 ( 10 ) type of excitation at harmonic force excitation 274 .........0 ( 0,1 - 4 ) selection: type of output list 275 ........0. ( x ) output limitation x to Opt.(274) 276 .........1 ( 1,2,3 ) output: node values as 1: displacement 2: velocity . 3: acceleration 277 .........0 ( 1 - 7 ) type of superposition at time history (SUPHA) 278 .........0 ( 1,2 ) type of superposition at response spectrum (SUPEV) 279 ........0. ( x ) x: magnification factor at SUPEV, valid for all . eigenvalues; for selected eigenv. via add. input 280 .....00000 ( 1-NDMAX ) node for frequency characteristic or response output . (from) 281 .....00000 ( 1-NDMAX ) end node to Opt.(280) (to) ----------------------------------------------------- Dynamics (eigenvalue calculation via matrix condensation (SMIS)) ----------------------------------------------------- 292 .........0 ( 1 ) 1: with differing masses load-case VN=99 and SMAS . 2: additional differing masses via additional input 293 .........0 ( 0 ) 0: HQRW-Algor. with double precision 1: standard-Alg. 294 .......-99 ( > 0 ) variant number > 0 of excitation SIMIT/SMIS . -99: superposition of all excitations 295 ........0. ( x ) x: tolerance value symmetry check K-matrix 296 .......000 ( i ) i: exponent to Opt.(295) 297 ........00 ( > 0 ) at quasi free/free > unused lower eigenvalues ----------------------------------------------------- Dynamics (response calculation with excitation (SMIS)) ----------------------------------------------------- 301 .......010 ( > 0 ) number of valid eigenvalues at response 302 .........0 ( 1 ) 0: degree of damping to Opt.(303) for all . eigenvalues, 1: damping matrix via additional input 303 ......0.05 ( x > 0. ) degree of damping as modal damping 304 .......000 ( i ) factor as exponent to radix 10 to Opt.(303) 305 ....0.0001 ( x > 0. ) integration interval / load increment 306 ........-2 ( i ) factor as exponent to radix 10 to Opt.(305) 307 ........00 ( > 0 ) number of calculated y-ordinates of . excitation function 308 ....0.0001 ( x > 0. ) x-interval y-ordinates calculation to Opt.(307) 309 ........-2 ( i ) factor as exponent to radix 10 to Opt.(308) 310 ........-2 (0,+-1,+-2 ) type of answer . 0: displacement 1: velocity 2: acceleration . -1: displacement + velocity -2: all 311 ........10 ( 0,1 ) output list interval to Opt.(305) . 1: for all steps 312 .........0 ( 1 ) using inital displacements via additional input 313 .........0 ( 1 ) using inital velocities via additional input 314 .........1 ( 0,1,2 ) excitation type 0:base excitation 1:force excitation . via excitation function . 2:calculate excitation forces . > additional input req. 315 ........00 ( max. 10 ) number of points at excitation function Opt.316-335 . 316 ........0. ( x0 > 0. ) x-value max. 10 points x and y of excitation function 317 ........0. ( y0 > 0. ) y-value at force excitation 318 ........0. ( x1 > 0. ) x-value 319 ........0. ( y1 > 0. ) y-value 320 ........0. ( x2 > 0. ) x-value 321 ........0. ( y2 > 0. ) y-value 322 ........0. ( x3 > 0. ) x-value 323 ........0. ( y3 > 0. ) y-value 324 ........0. ( x4 > 0. ) x-value (if more values necessary 325 ........0. ( y4 > 0. ) y-value define function via 326 ........0. ( x5 > 0. ) x-value additional input) 327 ........0. ( y5 > 0. ) y-value 328 ........0. ( x6 > 0. ) x-value 329 ........0. ( y6 > 0. ) y-value 330 ........0. ( x7 > 0. ) x-value 331 ........0. ( y7 > 0. ) y-value 332 ........0. ( x8 > 0. ) x-value 333 ........0. ( y8 > 0. ) y-value 334 ........0. ( x9 > 0. ) x-value 335 ........0. ( y9 > 0. ) y-value 336 ........0. ( x0 > 0. ) participation factor to define position and excitation 337 .......000 ( KKKKKI ) I: associated degree of freedom (1-6),KKKKK: node 338 ........0. ( x0 > 0. ) participation factor 339 .......000 ( KKKKKI ) I: associated degree of freedom (1-6),KKKKK: node 340 ........0. ( x0 > 0. ) participation factor 341 .......000 ( KKKKKI ) I: associated degree of freedom (1-6),KKKKK: node 342 ........0. ( x0 > 0. ) participation factor 343 .......000 ( KKKKKI ) I: associated degree of freedom (1-6),KKKKK: node 344 ........0. ( x0 > 0. ) participation factor 345 .......000 ( KKKKKI ) I: associated degree of freedom (1-6),KKKKK: node ----------------------------------------------------- Dynamics (list options (see list and stress output statics) ----------------------------------------------------- 347 .......000 (i= 1-122 ) all output suppressed (SIMIT) for eigenvalue i (from) 348 .......000 (j= 2-122 ) all output suppressed (SIMIT) until eigenvalue (to) 349 ........00 ( i ) each i.deformation (SMIS) as output list / file 350 .......000 ( j1 ) point of time Tj (SMIS) as output list / file 351 .......000 ( j2 ) point of time Tj (SMIS) as output list / file 352 .......000 ( j3 ) point of time Tj (SMIS) as output list / file 353 .......000 ( j4 ) point of time Tj (SMIS) as output list / file 354 .......000 ( j5 ) point of time Tj (SMIS) as output list / file ----------------------------------------------------- General or Weld Spot/Contact Options (linear and non-lin. STATIC, DYNAMIC) ----------------------------------------------------- 355 .........0 ( 0,1 ) 1: set all non-metal elements inactive, N-mm only 391 .........0 ( j=+/-ID ) ID=material ID inactive elements, start (-from) 392 .........0 ( j=+/-ID ) ID=material ID inactive elements, end (-to ) 393 .........0 ( j=+/-ID ) ID=material ID inactive elements, end (-to ) 394 .........0 ( j=+/-ID ) ID=material ID inactive elements, end (-to ) 356 ....camry3 ( 8 Charct.) net/layer liste name, extension *.wld . Format see user manual chap. 5.1.1 357 ...2000001 ( 1-2000 ) property number weld spots 358 .........1 ( 0,1 ) 0=rigid (RBE), 1=elastic (connection via bars) 359 .........1 ( 0,1,2 ) 0=no output, 1=connector-elements to wldel.out . 2 as 1, additional conact elem./nodes in *.lst 360 ....0.0833 (or greater) stiffness N/mm4 addtl. bars at master/slave contact ----------------------------------------------------- General: check print for internal values (e.g. matrices) at list . (XXXXXX) = subroutine name e.g. (STEMA) ----------------------------------------------------- 361 .........0 ( 1,2 ) edge and surface loads (RAND) 362 .........0 ( 1,10 ) Fourier analysis loads (FOURI); 10: approxim. contact 363 .........0 ( 1,2,3 ) calculated node forces of all load-cases (LASUM); . KEDA(ispru), KORAD 364 .........0 ( 1,2,3 ) mass forces (MAKRA), Medina/FEMAP-interface 365 .........3 ( 1,2,3 ) warping torsion (WOEDA), >1: switch off error K19 . 3: make 2 triangles if QUAD4 warping ang.>10.1° KEDA 366 .........0 ( 1,2,6 ) element data, element loads (STRUK) 367 .........0 ( 1...15 ) element matrix, global stiffness matrix (STEMA) 368 .......000 ( IIK ) equation solver, II=1-12 (subroutine), II=13 all, . K= 1-3 degree) (LIHS) 369 ....000000 ( i ) Opt. 368, from row i 370 ....000000 ( j ) Opt. 368, to row j 371 .........0 ( 1,2,3 ) new constraint equations, contact (AKNOS) 372 .........0 ( 1,2,3 ) nonlinear statics (TPSN) 373 .......000 ( IIK ) output list, II=1-10 (subroutine), K=1-4 (degree) . at STATICS (TEXT) and DYNAMICS (TEXT) 374 ...0000000 ( IIIIIIK ) dynamics(SIMIT), I=subroutine name, K=1-4(degree) 375 .........0 ( 1,2 ) dynamics(SMIS) 376 .........0 ( 1 ) back transformation excitation (SUPHA/SUPEV) 377 .........0 ( 1 ) matrix transformation at free/free (FREI) 378 .......000 ( IIK ) potential, element matrices, global matrix (TEMP) . II=1-8 (subroutine), K=1-4 (degree) 379 .......000 ( IIK ) output list potential (WTEXT) . II=1-4 (subroutine), K=1-3 (degree) 380 .........0 ( 1,2,3 ) temperature field plotting map (TEMPO) 381 .......000 ( IIK ) line plotting/HPGL (PLOT) . II=1-8 (subroutine), K=1-4 (degree) 382 .........0 ( 1 ) sort load-case data (SORT and MATREAD) 383 .........0 ( 1 ) subroutine names to screen ----------------------------------------------------- BEM-FEM-loop: in- and output control ----------------------------------------------------- 384 .........0 ( 0, 1, 2 ) homotopy parameter (U, Q, F), . 0=U: direct, 1=Q: charge, 2=F: force 385 ........ 1 ( 0, 1, 2 ) BEM input as *.lst file . 0: no, 1: at iteration end only, . 2: at each iteration 386 ........90 ( 0-xxx ) max. number of printed nodes at *.lst file 387 .........2 ( 0, 1, 2 ) type of termination (X, Q, F) . 0=X: geometric difference, 1=Q: relat. Q-difference, . 2=F: relat. force(F-)difference (F none scaled) 388 ...0.00001 ( x > 0. ) rel.termination precision QTOL,FTOL((A - Aold)/Aold) 389 .....0.003 ( x > 0. ) abs.termination precision TOLAB (A - A_old) 390 ........10 ( ) FEMAP node number for specific output ----------------------------------------------------- Important note! For the following entities additional input is required: ----------------------------------------------------- * supporting structures for weight/stiffness optimization (CT65) * new (changed) constraint equations (AKNOS) * extreme values calculation (EXTR) * node list at contact (KNOT) * mass forces (MAKR - FEMAP input possible) * wind loads (WIKR) * additional cross section values at warping stiffness or stress recovery(WOEDA) * advanced termination criterion at nonlinear statics (TPSN) * 3D nonlinear material (e.g. temp. dependent) nonlinear statics (TPSN) * edge flux calculation (RAND) * nonlinear material at steady state potential field * temperature field plotting map (TEMW) * variable constraints at dynamics (SIMI) * harmonic excitation etc. at dynamics (SIMI) * differing masses, damping matrix, participation factors etc. (SMIS) * line plotting as HPGL file (PLOT) ----------------------------------------------------- end of option file *** Database definition File record number path nbr. length of records ----------------------------------------------------- 1 4000 100 2 6000 50 3 1200 15000 4 1400 30000 5 1600 50000 6 18482500000 7 2000 250000 8 19203000000 9 6000 10000 10 12000 10000 11 8000 1000 12 1200 1000 13 18880 6000 14 1280 10000 15 1920 50000 16 1200 1 17 464404500000 18 464404500000 19 6000 100 20 9200 10000 21 5984 15000 22 46000 10000 23 464404500000 24 1600 50000 25 2080 10000 26 5200 100 27 2000 50000 28 1400 30000 29 14736 100000 30 6000 10000 31 1920 50000 32 464404500000 33 3200 50 34 46080 25000 35 7000 25000 36 3100 25000 37 3720 80 38 1800 10000 39 464404500000 40 46080 45000